Arduino Protocol

(start char)(command)(data)(end of data)(checksum)(end of transmission)

start char = x01
command (2 bytes)
data (variable length)
(datatype)(data)...(data)(delimiter)
datatypes : C (x54) – text (char 16 bit ASCII)
     A (x52) – ASCII char (8 bit)
     X (x58) – binary – escape char = “\” (x5C)
        I (x49) – int (32 bit)
     D (x44) – double (64 bit)
     F (x46) – float (16 bit)
     L (x4C) – long (64 bit)
     B (x42) – BOOLEAN (T/F = x54/x46)
delimiter : x1E
end of data = x03
checksum (1 byte) = CRC function
end of transmission = x04

CRC
//CRC-8 - based on the CRC8 formulas by Dallas/Maxim
//code released under the therms of the GNU GPL 3.0 license
byte CRC8(const byte *data, byte len) {
  byte crc = 0x00;
  while (len--) {
    byte extract = *data++;
    for (byte tempI = 8; tempI; tempI--) {
      byte sum = (crc ^ extract) & 0x01;
      crc >>= 1;
      if (sum) {
        crc ^= 0x8C;
      }
      extract >>= 1;
    }
  }
  return crc;
}

HELLO/WORLD : x00x01

Used to establish/validate contact. If a “hello” message is received, respond with “world”

(HELLO) : x01x00x01x54x48x45x4Cx4Cx4Fx1Ex03[CHECKSUM]x04
(WORLD) : x01x00x01x54x57x4Fx52x4Cx44x1Ex03[CHECKSUM]x04

SET LOG LEVEL : x00x02

Sets the log level of the serial communication handler.
0 = NONE, completely silent
1 = ERROR, reports only errors
2 = STATUS, reports on message receipt, etc.
3 = DEBUG, reports everything

(SET LOG LEVEL to 2) : x01x00x02x58x02x1Ex03[CHECKSUM]x04

GET TIME : x00x10

Used to solicit time from partner.

(request)	: x01x00x10x03[CHECKSUM]x04
(response)	: x01x00x10x4C[time, long – 8 bytes]x1Ex03[CHECKSUM]x04

SET TIME : x00x11

Used to sync time between partners.

x01x00x11x4C[time, long – 8 bytes]x1Ex03[CHECKSUM]x04

GET STATUS : x00x15

Used to get status of all arduino input/output points. It request data specifies the point using a bit representation.

00000000 00000000 00000001 A0 (x00x00x01)
00000000 00000000 00000010 A1 (x00x00x02)
…
00000000 00000000 00100000 A5 (x00x00x20)
00000000 00000000 01000000 D0 (x00x00x04)
00000000 00000000 10000000 D1 (x00x00x08)
…
00001000 00000000 00000000 D13 (x08x00x00)

00001111 11111111 11111111 ALL (x0FxFFxFF)

request :
x01x00x15x58(3 bytes)x1Ex03[CHECKSUM]x04

response :
x01x00x15(type)(ADC0)x1E...(type)(ADC5)x1E(type)(PD2)x1E...(type)(PD7)x1E(type)(PB0)x1E...(type)(PB5)x1Ex03[CHECKSUM]x04

SET STATUS : x00x16

Used to override the analog in or the digital out value. The correct behavior for the analog inputs is to latch (stop sampling) to the given value. Data is “A” or “D” (x41 or x44) followed by x00 – x0C.

(Set D1 ON) : x01x00x16x58x44x01x1Ex42x54x1Ex03[CHECKSUM]x04

RELEASE STATUS : x00x17

Used to release an “SET STATUS” command. Uses the same addressing as “GET STATUS”

(release A2,A4,D1,D2 & D11)
DATA : 000000010 00000001 10010100 = x02x01x94
message : x01x00x17x58x02x01x94x1Ex03[CHECKSUM]x04